## Slide 1: TCP Communication using Cavli Modules

## Slide 2: Socket Communication
A method for exchanging data between devices over a network
Uses a combination of IP address and port number
Enables connection to remote servers or other devices
Supports protocols like TCP and UDP
Commonly used in IoT and embedded systems
Facilities reliable data transfer between module and cloud/server

## Slide 3: Overview of C10GS Module
Compact LTE CAT‑1/4 module
Dual-core ARM11 at 400 MHz
Interfaces: USB, UART, SPI, I2C
Supports: TCP/IP, HTTP, MQTT, FTP

## Slide 4: TCP/IP AT‑Command Architecture
Embedded TCP/IP stack
Three access modes:
1. Buffer mode
2. Direct push mode
3. Transparent mode

## Slide 5: AT+QIOPEN – Open Socket
Syntax:
AT+QIOPEN=<ctxID>,<connID>,"TCP","<IP>",<port>,<lport>,<mode>
Returns OK, then:
+QIOPEN: <connID>,<err>

## Slide 6: Example: Opening TCP Client
AT+QIDEACTEX=1
AT+QIACT=1
AT+QIOPEN=1,0,"TCP","192.168.1.100",5000,0,1
URC: +QIOPEN: 0,0 → Success

## Slide 7: AT+QISEND – Transmit Data
AT+QISEND=<connID>,<length>
> Sensor data<CTRL+Z>
Response: SEND OK / FAIL / ERROR
Check ack: AT+QISEND=<connID>,0

## Slide 8: Data Receive Methods
- Buffer mode: AT+QIRD=<connID>,<len>
- Direct push: URC includes data
+QIURC: "recv",0,20
<20 bytes payload>

## Slide 9: Example: Full Workflow
1. AT+QIACT=1
2. AT+QIOPEN=...
3. AT+QISEND=0,15
4. Receive via URC
5. AT+QICLOSE=0

## Slide 10: Access Mode Comparison
Mode | AT Cmds | Flow | Exit
0 Buffer | Yes | AT+QIRD | QICLOSE
1 Direct | Yes | URC | QICLOSE
2 Transparent | No | End-to-end | +++

## Slide 11: Summary
C10GS supports full TCP stack
AT+QIOPEN for socket
AT+QISEND for data
Multiple modes available

## Slide 12: References
Cavli C10GS Docs
Quectel TCP/IP AT Cmds Guide